OSMOMETER

INSTRUCTIONS FOR USE:

TO CALIBRATE (must do before initial session use)

- Turn handle on right side of osmometer to “OPEN”

- Pull out the (lower) white sample bar on the front of the osmometer

- Put clean, dry sample disc on the silver sample tray on the white bar (using forceps)

- Add 10l 290mosm standard to sample disc

- Close sample tray/bar and turn handle on the right side of osmometer to “CLOSE”

- Osmometer will read sample – finished when “In Process” light turns off.

- Adjust “calibrate 290” dial on top of osmometer until readout on front = 290

- Clean.

TO READ SAMPLE

- Turn handle on right side of osmometer to “OPEN”

- Pull out the (lower) white sample bar on the front of the osmometer

- Put clean, dry sample disc on the silver sample tray on the white bar (using forceps)

- Add 10l sample solution to sample disc

- Close sample tray/bar and turn handle on the right side of osmometer to “CLOSE”

- Osmometer will read sample – finished when “In Process” light turns off.

- Clean.

TO CLEAN

- After finished with sample reading, turn handle on right side of osmometer to “OPEN”

- Pull out the (lower) white sample bar on the front of the osmometer

- Remove sample disc from tray using cotton tipped applicator

- Add drop of diH20 to tray, swab with cotton tipped applicator to remove water

- When completely dry, close sample tray/bar and turn handle to “CLOSE”