## Slide 1: Greening Backbone Networks Shutting Off Cables in Bundled Links
Will Fisher, Martin Suchara,
and Jennifer Rexford
Princeton University

## Slide 2: Why Focus on Networks?
Saving energy in servers vs. networks
Potential for savings in wired networks
  $2 billion annual power bill in USA alone
  Over-engineering and diurnal patterns
  Power draw does not scale with load

## Slide 3: Power Consumption of Network Hardware
Router may consume 200 - 400W plus 100 W per line card
  Power draw does not scale with load
chassis
line card

## Slide 4: Turn Off Unneeded Routers / Links?
Turning off links has drawbacks
  Increased RTT, fragility, etc.

## Slide 5: Links in Large Backbone Networks
Links come in bundles
  Gradual upgrades, hardware costs, etc.
City B
City A

## Slide 6: Links in Large Backbone Networks
Links come in bundles
  Gradual upgrades, hardware costs, etc.
In large networks
  Majority of links bundled
  Bundle sizes 2 – 20 cables per link
Bundled link behaves as a single logical link

## Slide 7: The Problem…
Powering all cables is wasteful
City B
City A
30-40% utilization

## Slide 8: Proposed Solution
Only power up cables that are needed
  Transparent to routing protocols
80% utilization
City B
City A

## Slide 9: Overview
Optimization problem formulation & solution
Experimental evaluation of energy savings
Conclusion

## Slide 10: The Problem
Algorithm used by network operators
  Input: network configuration and load
  Output: list of powered cables
min # powered cables
s.t. link loads ≤ capacities
flow conservation
carries all traffic demands
NP-hard in general → need heuristics
Integer linear program:

## Slide 11: Related Tractable Problem
How would the solution look like if energy consumption was proportional to link load
Benefits: tractable, provides upper and lower bound on potential power saving, starting point for heuristics
Minimize sum of link loads rather than the number of powered cables
  Fractional vs. integer linear program

## Slide 12: First Attempt – Naïve Solution
Always round up:
→
Up to n times worse performance where n ≈ number of cities

## Slide 13: Three Increasingly Sophisticated Heuristics
Start with the naïve solution and perform local search
Fast Greedy Heuristic (FGH)
Exhaustive Greedy Heuristic (EGH)
Bi-level Greedy Heuristic (BGH)

## Slide 14: The Fast Greedy Heuristic (FGH)
1. solve the fractional linear program
and round up
2. identify link with greatest
rounding up
→
3. round down by permanently removing
one more cable in that link
4. goto step 1 if feasible solution
exists

## Slide 15: Overview
Optimization problem formulation & solution
Experimental evaluation of energy savings
Conclusion

## Slide 16: Experimental Setup
Solve the simple linear program using AMPL / CPLEX
Experiments repeated for bundle sizes 1 to 12
Determine energy savings and ability to run algorithms in real time

## Slide 17: Topologies
Abilene with real measured traffic demands
Waxman and hierarchical topologies

## Slide 18: Energy Savings– Abilene Topology
Energy savings depend on the bundle size.
energy savings (%)
bundle size
Turn entire link on or off
Similar performance of heuristics

## Slide 19: Waxman and Hierarchical Graphs
Turn entire link on or off
The same general trend

## Slide 20: Execution Time
FGH is well suited for real-time execution
Topology | FGH | EGH | BGH
Abilene | 8 sec | 50 sec | 5 min
Large synthetic | minutes | minutes to hours | 

## Slide 21: Overview
Optimization problem formulation & solution
Experimental evaluation of energy savings
Conclusion

## Slide 22: Conclusion
Powering all links in a bundle usually not needed
Design and evaluation of simple heuristics
  Significant energy savings
  Low computational complexity
  Can choose the simplest heuristic (FGH)

## Slide 23: Thank You!